## Slide 1: Fancy Math for a Stupid Chat
By Milkey Mouse

## Slide 2: I just feel like somebody’s watching me
School tracks all Wi-Fi, Bluetooth, and radio communications from any school computer
DyKnow makes the situation even worse if you’re not in Safe Mode
If you’re on your own device and connected to LWSD-GUEST they also track you
They scramble signals from cell towers so nobody uses their data plan
Their Microsoft Exchange server is set to keep all emails and conversations for 100 days after deletion, even if perma-deleted by the user
But the one thing they DON’T track…

## Slide 3: AUDIO!

## Slide 4: Audio as a Transport
It’s just too weird for them to think of
Why would DyKnow need audio mirroring?
Worst case scenario some kid is listening to Justin Bieber, right?
WRONG!
By using sound you can transfer quite a bit of data (I’ll get back to this in a second)

## Slide 5: But wait, there’s more
The Mosquito Tone
  Invented by a shopkeeper and an age-discriminatory sonic weapon
  It would make an interesting argumentative essay
  Very high-pitched
  Can only be heard by people under 25 (so no teacher snooping!)
    The cutoff age can change by changing the frequency minute amounts
No known side effects

## Slide 6: Transmission Formats (or encodings, as they’re known in the 1337 h4x0r biz)
Using different frequencies (and rounding to the nearest bin in case of error) for multiple characters
Morse code (…---…)
  Pretty much the original, used as early as 1844
  Very good margins for error with only 2 possibilities
  But slooow
    If each dot took 0.2 seconds and each dash took 0.5, this would take 1.8 seconds to transmit the word “sos”
ASCII
  128 characters of stuff
  What early computers/computer enthusiasts used
  Only Latin characters, numbers, and some punctuation
  Needless to say, that’s not what they use today
  Margin for error would be too small with 128 discrete frequencies/”bins”
Base64
  Uses only 64 characters to represent any other character, it just takes more of them
  Doubles the size of each bin for the frequencies
Base32
  Like Base64, but uses 32 characters instead of 64 and the resulting messages are even longer
  Doubles the margins again from Base64
So I chose Base32, because after testing even Base64 didn’t have small enough bins.
On the bright side, the bins of each frequency are so large that each character can be transmitted in under 0.1 seconds.

## Slide 7: Now how to generate the sound?
If using Base32/Base64, encode the message now
Get a numerical index for each character
For each resulting number, multiply by 100 and add 17000 Hz (just a little bit below the Mosquito Tone). Save this to an audio file in memory, so it never gets stored on the hard drive and becomes trackable.
Play the audio file at full volume. (Since the sounds are so high-pitched, it doesn’t matter how loud it is.
“Hello World”
“JJBSWY3DPEBLW64TM MQ= = = = = =”
[9, 9, 1, 18, 22, 24, 27, 3, 15, 4, 1, 11, 22, 30, 28, 19, 12, 33, 12, 16, 32, 33, 32, 33, 32, 33, 32, 33, 32, 33, 32]

## Slide 8: But there’s another problem…

## Slide 9: WARNING: MATH INCOMING

## Slide 10: The Zero-Crossing Algorithm
3 ÷ 2 = 1.5
1
2
3
Just count the times the wave crosses zero!
I saw a sine
And it was made of points and lines

## Slide 11: Problems with the Zero-Crossing Algorithm
+
Ultrasonic frequency
Audible frequency (e.g. talking)
=
A weird thing
All fine and dandy when the ultrasound is louder than the speech…
closer to this one
Result is the same as that of the ultrasonic transmission

## Slide 12: Problems with the Zero-Crossing Algorithm
+
Ultrasonic frequency
Audible frequency (e.g. talking)
=
An even weirder thing
…but when talking is louder than the transmission it wonks out (the technical term)
closer to this one
Result is the same as the talking!


## Slide 13: So with any noise in the background the Zero Crossing Algorithm won’t work.

## Slide 14: Enter Fast Fourier Transform (FFT)
Wonky wave
(pronounced four-ee-yay)
FFT!
An FFT outputs a nice pretty histogram of possible frequencies.

## Slide 15: How does it do this?

## Slide 16: Math too complicated to go into here.

## Slide 17: Enter Fast Fourier Transform (FFT)
(pronounced four-ee-yay)
Now let’s take a look at that histogram, shall we?
Frequency
Amplitude
Possible Frequencies in Captured Sound

## Slide 18: Enter Fast Fourier Transform (FFT)
(pronounced four-ee-yay)
First order of business: cut off the audible range
Frequency
Amplitude
Possible Frequencies in Captured Sound
All of these are probably talking, as they’re in the audible range…

## Slide 19: Enter Fast Fourier Transform (FFT)
(pronounced four-ee-yay)
Then we get the frequency over the threshold
Frequency
Amplitude
Possible Frequencies in Captured Sound
…so we chop them all off!
Next we find the highest one above our threshold…
And voila! Here’s the frequency we were looking for.

## Slide 20
As evidenced by the heights of the original audible peaks, the FFT algorithm filters noise very well and can be used to pick up transmissions even from across the room!
Frequency
Amplitude
Possible Frequencies in Captured Sound
All of these are probably talking, as they’re in the audible range…

## Slide 21: Conversion back to text is pretty much the same but backwards
Stream audio from the mic and run FFTs until you get outlier frequencies (the FFT conveniently has bin sizes of 100 by default)
With the same conversion table as last time, turn the numbers back into letters and process the data.
Use Base64/Base32 if needed to decode the message into a string again.
“Hello World”
“JBSWY3DPEBLW64TMMQ======”
[9, 9, 1, 18, 22, 24, 27, 3, 15, 4, 1, 11, 22, 30, 28, 19, 12, 33, 12, 16, 32, 33, 32, 33, 32, 33, 32, 33, 32, 33, 32]

## Slide 22: But what if you’re really far away?

## Slide 23: Take clues from torrents and make it P2P

## Slide 24: And have error correction
OK
lolwut
Sos
OK

## Slide 25: And have error correction
Oh OK
He said, “Sos”

## Slide 26: Or even pipe internet
Get me “blocked.com”
Here is blocked.com
Crappy School Internet
You can’t have “blocked.com”
Legit Internet
Fine then. Ultrasound Node, get me “blocked.com”

## Slide 27: Messages are above the hearing ranges of most people above 25

## Slide 28: And who knows, maybe we won’t get caught this time.

## Slide 29: Time for a demo!